## Slide 1: Wireshark Dissectors
3 ways to eat bytes
Graham Bloice – Software Developer

## Slide 2: Introduction
Software Developer with Trihedral UK Limited
  Use C++ and scripting for SCADA toolkit VTScada™
  Use Wireshark with industrial tele-control protocols
Wireshark Core Developer
  First contributed to Wireshark in 1999
  Maintain DNP3 dissector
  Frequent contributor to “Ask Wireshark”
    Mostly fixing formatting and converting “answers” to comments 

## Slide 3: Topics to be Covered
Wireshark internals brief overview
  Where dissectors fit in
Dissectors
  Brief overview
  Paths to implementation
  Complexity and performance tradeoffs

## Slide 4: Wireshark Internals
Wireshark provides a framework for loading, dissection and visualization of network traffic
Wireshark framework allows individual dissectors access to network data via libwiretap
Wireshark framework provides utility functions for dissectors when dissecting data
Wireshark framework allows dissectors to write out products of dissection

## Slide 5: Dissectors overview
Dissectors “register” their interest in data from a lower level protocol dissector, e.g. tcp port 54321
The lower level dissector hands the payload body to the registered dissector
Dissectors “pick apart” a protocol into the individual elements of the protocol message
Each element of a protocol may have a type, e.g. integer, string, bit field, timestamp
Dissectors provide elements that may be used in display filters

## Slide 6: Dissector output
Set the protocol column
Set the info column
Create tree entries as required
  Create subtree entries for protocol components
  Add values, text to tree entries
Call sub-dissectors as required

## Slide 7: Dissector Construction Options
Text based
  Built-in, with compilation – ASN.1, IDL
  External, without compilation – Wireshark Generic Dissector (WSGD)*
Scripting language based
  Built-in, Lua*, Python (not in Windows)
  External, Python (pyreshark)
C based*
  Traditional format, requires a development environment

## Slide 8: Demonstration protocol
Made up for this presentation
Has a header with a byte indicating the message type, and a short (2 bytes in big-endian format) for the total message length (including the header)
Commands are:
  connect (20) and connect_ack (21) that have a long (4 bytes in little-endian format) id
  disconnect (60) and disconnect_ack (61) that have a long (4 bytes in little-endian format) id
  request_data and request_reply that have a byte indicating the data type and for the reply an actual data value;
    Data type 0 – a little-endian short
    Data type 1 – a little-endian long
    Data type 2 – a 15 character string

## Slide 9: Text based Dissectors
Protocol definition held in text file(s) in human readable form
Definitions are interpreted or compiled to produce a dissector
Low barrier to entry, although ASN.1 and IDL requires a development environment to compile resulting dissector
Interpreted text files are least performant option
Least flexible option for access to libwireshark infrastructure

## Slide 10: Wireshark Generic Dissector (WSGD)
A Wireshark add-on created by Olivier Aveline, info at http://wsgd.free.fr/
Allows dissection of a protocol based on a text description of the protocol elements
Available for Windows and Linux as a plug-in module
Has some limitations but relatively simple to use and doesn’t require a development environment

## Slide 11: WSGD Dissectors
Copy the appropriate version of the plugin into your Wireshark installation:
  Global plugins
  Personal plugins
Copy (or create) the definition files in the required location:
  As specified by the environment variable “WIRESHARK_GENERIC_DISSECTOR_DIR”
  Profiles directory
  User data directory
  Global plugin directory
  Wireshark main directory

## Slide 12: WSGD Basics – Protocol Definition
# Protocol identification
PROTONAME SharkFest 14 Protocol (WSGD)
PROTOSHORTNAME SF14
PROTOABBREV sf14
# Protocol parent, controls when dissector is called
PARENT_SUBFIELD tcp.port
PARENT_SUBFIELD_VALUES 54321
# Message header, protocol starts with a header
MSG_HEADER_TYPE T_msg_header
# Message type identifier, must be part of header
MSG_ID_FIELD_NAME Function
# Message title field, shown in Info column
MSG_TITLE InfoString
# Message size field, from field in header
MSG_TOTAL_LENGTH Length
# Message body type:
MSG_MAIN_TYPE T_msg_switch(Function)
# Field definitions
PROTO_TYPE_DEFINITIONS
include sf14.fdesc;

## Slide 13: WSGD Basics – Field Definitions I
# Message type enumeration
enum8 T_Type_message
{
connect 20 # must be an integer
connect_ack - # "-" indicates previous value + 1
request_data 40
request_reply -
disconnect 60
disconnect_ack -
}
# Header definition
struct T_msg_header
{
byte_order big_endian;
T_Type_message Function;
uint16 Length;
hide var string InfoString = print ("%s", Function); # Note type conversion
byte_order little_endian;
}

## Slide 14: WSGD Basics – Field Definitions II
# Messages
struct T_msg_connect
{
T_msg_header Header;
uint32 ID;
}
struct T_msg_connect_ack
{
T_msg_header Header;
uint32 ID;
}
struct T_msg_disconnect
{
T_msg_header Header;
uint32 ID;
}
struct T_msg_disconnect_ack
{
T_msg_header Header;
uint32 ID;
}

## Slide 15: WSGD Basics – Field Definitions III
# Data value enumeration
enum8 T_Type_dataid
{
read_short 0
read_long 1
read_string 2
}
struct T_msg_request_data
{
T_msg_header Header;
T_Type_dataid Data_ID;
}
struct T_msg_request_reply
{
T_msg_header Header;
T_Type_dataid Data_ID;
switch(Data_ID)
{
case T_Type_dataid::read_short : uint16 Data_Short;
case T_Type_dataid::read_long : uint32 Data_Long;
case T_Type_dataid::read_string : string(15) Data_String;
}
}
struct T_msg_unknown
{
T_msg_header Header;
raw(*) end_of_msg;
}

## Slide 16: WSGD Basics – Field Definitions IV
# Main switch
switch T_msg_switch T_Type_message
{
case T_Type_message::connect : T_msg_connect "";
case T_Type_message::connect_ack : T_msg_connect_ack "";
case T_Type_message::request_data : T_msg_request_data "";
case T_Type_message::request_reply : T_msg_request_reply "";
case T_Type_message::disconnect : T_msg_disconnect "";
case T_Type_message::disconnect_ack : T_msg_disconnect_ack "";
default : T_msg_unknown "";
}

## Slide 17: Scripting language based dissectors
Protocol definition held in text file(s) using the script language syntax
Definitions are interpreted by the scripting language run-time
Scripting run-time exposes access to libwireshark infrastructure
Not all libwireshark infrastructure exposed
No development environment required
Faster than text dissectors, slower than C

## Slide 18: Lua dissectors
Lua is built-in to Wireshark (on most platforms)
The lua support can be used to build dissectors, post-dissectors and taps
init.lua in the global configuration directory is run at Wireshark start-up
If disable_lua is not set to 0 runs init.lua from the personal configuration directory
Loads all lua scripts (*.lua) in the global and personal plugins directory
Runs any scripts passed on the command line with –X lua_script:xxx.lua

## Slide 19: Lua dissector Basics – Protocol definition
-- declare the protocol
sf14_proto = Proto("sf14", "SharkFest'14 Protocol (lua)")
-- declare the value strings
local vs_funcs = {
[20] = "connect",
[21] = "connect_ack",
[40] = "request_data",
[41] = "request_reply",
[60] = "disconnect",
[61] = "disconnect_ack"
}
local vs_dataid = {
[0] = "read short",
[1] = "read long",
[2] = "read string"
}

## Slide 20: Lua dissector Basics – Field definition
-- declare the fields
local f_func = ProtoField.uint8("sf14.func", "Function", base.DEC, vs_funcs)
local f_len = ProtoField.uint16("sf14.len", "Length", base.DEC)
local f_id = ProtoField.uint32("sf14.id", "ID", base.DEC)
local f_dataid = ProtoField.uint8("sf14.data.id", "Data ID", base.DEC, vs_dataid)
local f_data_short = ProtoField.int16("sf14.data.short", "Data Short", base.DEC)
local f_data_long = ProtoField.int32("sf14.data.long", "Data Long", base.DEC)
local f_data_string = ProtoField.string("sf14.data.string", "Data String")
sf14_proto.fields = { f_func, f_len, f_id, f_dataid,
f_data_short, f_data_long, f_data_string }

## Slide 21: Lua dissector Basics – Dissector function I
function sf14_proto.dissector(buffer, pinfo, tree)
-- Set the protocol column
pinfo.cols['protocol'] = "SF14"
-- create the SF14 protocol tree item
local t_sf14 = tree:add(sf14_proto, buffer())
local offset = 0
-- Add the header tree item and populate it
local t_hdr = t_sf14:add(buffer(offset, 3), "Header")
local func_code = buffer(offset, 1):uint()
t_hdr:add(f_func, func_code)
t_hdr:add(f_len, buffer(offset + 1, 2))
offset = offset + 3
-- Set the info column to the name of the function
pinfo.cols['info'] = vs_funcs[func_code]
-- dissect common part for connect and disconnect functions
if func_code == 20 or func_code == 21 or func_code == 60 or func_code == 61 then
-- A connect or connect ack or disconnect or disconnect_ack
t_sf14:add_le(f_id, buffer(offset, 4))
end

## Slide 22: Lua dissector Basics – Dissector function II
-- A request_data or request_reply message
if func_code == 40 or func_code == 41 then
-- dissect common part of request functions
t_sf14:add(f_dataid, buffer(offset, 1))
-- dissect request_reply data body
if func_code == 41 then
-- A request_reply
local dataid = buffer(offset, 1):uint()
offset = offset + 1
if dataid == 0 then
-- a read short data item
t_sf14:add_le(f_data_short, buffer(offset, 2))
end
if dataid == 1 then
-- a read long data item
t_sf14:add_le(f_data_long, buffer(offset, 4))
end
if dataid == 2 then
-- a read string data item
t_sf14:add(f_data_string, buffer(offset, 15))
end
end
end
end

## Slide 23: Lua dissector Basics – Dissector registration
-- load the tcp port table
tcp_table = DissectorTable.get("tcp.port")
-- register the protocol to port 54321
tcp_table:add(54321, sf14_proto)

## Slide 24: C based dissectors
Protocol definition, implied in dissector source
Dissector source file compiled into libwireshark or as a plugin
All libwireshark infrastructure available
Full development environment required
High knowledge barrier to initial implementation
Use existing dissectors as a guide
Developers Guide is essential reading, also README.developer

## Slide 25: C dissector installation
Place source file in epan\dissectors
Add entry for source to Makefile.common, epan\CMakeLists.txt
Quick test compile in the dissectors directory, e.g. nmake –f Makefile.nmake packet-sf14.obj
Rebuild Wireshark in the normal way

## Slide 26: C dissector – preliminary declarations
#include "config.h"
#include <glib.h>
#include <epan/packet.h>
#define SF14_PORT 54321
#define FUNC_CONNECT 20
#define FUNC_CONN_ACK 21
#define FUNC_REQ_DATA 40
#define FUNC_REQ_REPLY 41
#define FUNC_DISCONNECT 60
#define FUNC_DISC_ACK 61
/* A sample #define of the minimum length (in bytes) of the protocol data.
* If data is received with fewer than this many bytes it is rejected by
* the current dissector. */
#define SF14_MIN_LENGTH 4
static const value_string sf14_func_vals[] = {
{ FUNC_CONNECT, "connect" },
{ FUNC_CONN_ACK, "connect_ack" },
{ FUNC_REQ_DATA, "request_data" },
{ FUNC_REQ_REPLY, "request_reply" },
{ FUNC_DISCONNECT, "disconnect" },
{ FUNC_DISC_ACK, "disconnect_ack" },
{ 0, NULL }
};
#define READ_SHORT 0
#define READ_LONG 1
#define READ_STRING 2
static const value_string sf14_data_type_vals[] = {
{ READ_SHORT, "read short" },
{ READ_LONG, "read long" },
{ READ_STRING, "read string" },
{ 0, NULL }
};
/* Initialize the protocol and registered fields */
static int proto_SF14 = -1;
static int hf_SF14_Func_Code = -1;
static int hf_SF14_Length = -1;
static int hf_SF14_ID = -1;
static int hf_SF14_Data_ID = -1;
static int hf_SF14_Data_Short = -1;
static int hf_SF14_Data_Long = -1;
static int hf_SF14_Data_String = -1;
/* Initialize the subtree pointers */
static gint ett_SF14 = -1;
static gint ett_SF14_hdr = -1;

## Slide 27: C dissector – dissection function I
/* Code to actually dissect the packets */
static int
dissect_SF14(tvbuff_t *tvb, packet_info *pinfo, proto_tree *tree, void *data _U_)
{
/* Set up structures needed to add the protocol subtree and manage it */
proto_item *ti, *hdr_ti;
proto_tree *SF14_tree, *SF14_hdr_tree;
/* Other misc. local variables. */
guint offset = 0;
guint8 func_code;
guint8 data_id;
/* Check that there's enough data */
if (tvb_length(tvb) < SF14_MIN_LENGTH)
return 0;
/* Fetch some values from the packet header using tvb_get_*(). If these
* values are not valid/possible in your protocol then return 0 to give
* some other dissector a chance to dissect it.
*/
func_code = tvb_get_guint8(tvb, offset);
if (try_val_to_str(func_code, sf14_func_vals) == NULL)
return 0;
/*** COLUMN DATA ***/
/* Set the Protocol column to the constant string of sf14 */
col_set_str(pinfo->cinfo, COL_PROTOCOL, "SF14");
col_clear(pinfo->cinfo, COL_INFO);
col_add_str(pinfo->cinfo, COL_INFO,
val_to_str(func_code, sf14_func_vals, "Unknown function (%d)"));

## Slide 28: C dissector – dissection function II
/*** PROTOCOL TREE ***/
/* create display subtree for the protocol */
ti = proto_tree_add_item(tree, proto_SF14, tvb, 0, -1, ENC_NA);
SF14_tree = proto_item_add_subtree(ti, ett_SF14);
/* create subtree for the header */
hdr_ti = proto_tree_add_text(SF14_tree, tvb, 0, 3, "Header");
SF14_hdr_tree = proto_item_add_subtree(hdr_ti, ett_SF14_hdr);
/* Add an item to the subtree, see section 1.6 of README.developer for more
* information. */
proto_tree_add_item(SF14_hdr_tree, hf_SF14_Func_Code, tvb, offset, 1, ENC_LITTLE_ENDIAN);
offset += 1;
/* Continue adding tree items to process the packet here... */
proto_tree_add_item(SF14_hdr_tree, hf_SF14_Length, tvb, offset, 2, ENC_BIG_ENDIAN);
offset += 2;
/* Now add items depending on the specific function code */
switch (func_code)
{
case FUNC_CONNECT:
case FUNC_CONN_ACK:
case FUNC_DISCONNECT:
case FUNC_DISC_ACK:
proto_tree_add_item(SF14_tree, hf_SF14_ID, tvb, offset, 4, ENC_LITTLE_ENDIAN);
offset += 1;
break;

## Slide 29: C dissector – dissection function III
case FUNC_REQ_DATA:
case FUNC_REQ_REPLY:
/* Dissect the common portion of the two functions */
data_id = tvb_get_guint8(tvb, offset);
proto_tree_add_item(SF14_tree, hf_SF14_Data_ID, tvb, offset, 1, ENC_LITTLE_ENDIAN);
offset += 1;
if (func_code == FUNC_REQ_REPLY) {
switch (data_id)
{
case READ_SHORT:
proto_tree_add_item(SF14_tree, hf_SF14_Data_Short, tvb, offset, 2, ENC_LITTLE_ENDIAN);
offset += 2;
break;
case READ_LONG:
proto_tree_add_item(SF14_tree, hf_SF14_Data_Long, tvb, offset, 4, ENC_LITTLE_ENDIAN);
offset += 4;
break;
case READ_STRING:
proto_tree_add_item(SF14_tree, hf_SF14_Data_String, tvb, offset, 15, ENC_LITTLE_ENDIAN);
offset += 15;
break;
default:
break;
}
}
break;
default:
break;
}
/* Return the amount of data this dissector was able to dissect (which may
* or may not be the entire packet as we return here). */
return offset;
}

## Slide 30: C dissector – protocol registration I
void
proto_register_SF14(void)
{
/* Setup list of header fields See Section 1.6.1 of README.developer for
* details. */
static hf_register_info hf[] = {
{ &hf_SF14_Func_Code,
{ "Function", "sf14.func",
FT_UINT8, BASE_DEC, VALS(sf14_func_vals), 0x0,
"Message Function Code Identifier", HFILL }
},
{ &hf_SF14_Length,
{ "Length", "sf14.len",
FT_UINT16, BASE_DEC, NULL, 0x0,
"Message Length", HFILL }
},
{ &hf_SF14_ID,
{ "ID", "sf14.id",
FT_UINT32, BASE_DEC, NULL, 0x0,
"Connection ID", HFILL }
},
{ &hf_SF14_Data_ID,
{ "Data_ID", "sf14.data.id",
FT_UINT8, BASE_DEC, VALS(sf14_data_type_vals), 0x0,
"Data Type Identifier", HFILL }
},
{ &hf_SF14_Data_Short,
{ "data_short", "sf14.data.short",
FT_UINT16, BASE_DEC, NULL, 0x0,
"Data Short", HFILL }
},
{ &hf_SF14_Data_Long,
{ "data_long", "sf14.data.long",
FT_UINT32, BASE_DEC, NULL, 0x0,
"Data Long", HFILL }
},
{ &hf_SF14_Data_String,
{ "data_string", "sf14.data.string",
FT_STRING, BASE_NONE, NULL, 0x0,
"Data String", HFILL }
},
};

## Slide 31: C dissector – protocol registration II
/* Setup protocol subtree array */
static gint *ett[] = {
&ett_SF14,
&ett_SF14_hdr
};
/* Register the protocol name and description */
proto_SF14 = proto_register_protocol("SharkFest'14 Protocol (C)", “SF14", "sf14");
/* Required function calls to register the header fields and subtrees */
proto_register_field_array(proto_SF14, hf, array_length(hf));
proto_register_subtree_array(ett, array_length(ett));
}
/* Simpler form of proto_reg_handoff_SF14 which can be used if there are
* no prefs-dependent registration function calls. */
void
proto_reg_handoff_SF14(void)
{
dissector_handle_t SF14_handle;
/* Use new_create_dissector_handle() to indicate that dissect_SF14()
* returns the number of bytes it dissected (or 0 if it thinks the packet
* does not belong to SF14).
*/
SF14_handle = new_create_dissector_handle(dissect_SF14, proto_SF14);
dissector_add_uint("tcp.port", SF14_PORT, SF14_handle);
}

## Slide 32: Comparison of dissectors
For this simple “protocol”, Wireshark displays are almost identical
WSGD and Lua dissectors are quick and easy to develop; edit file and restart Wireshark
WSGD facilities are most limited option, Lua more advanced
C dissectors easy to distribute, build an installer package, easy to contribute back to Wireshark
WSGD 124 lines, Lua 89 lines, C 270 lines

## Slide 33: Comparison of dissectors performance
No visible difference for a small capture file, 11 packets
Medium capture file (~ 1M packets) results:
  WSGD: 2:16
  Lua: 0:39
  C: 0:20

## Slide 34: Questions?
Other dissector options?
Future directions?